## Supported Mathematical Functions, Operators and Constants

Mathematical functions:

| Function Name | Alternate Name | Parameters | Description | Notes |
| --- | --- | --- | --- | --- |
| if | — | (test,a,b) | If-else function. If the test returns true, the result is a, else it returns b. | Example: B1 out 0 V={if(v(1)>5, v(1)**2, 0)} |
| sin | sine | ( x ) | Sine function. | — |
| asin | arcsin | ( x ) | Arc-sine function. | — |
| sinh | — | ( x ) | Hyperbolic sine function. | — |
| asinh | arcsinh | ( x ) | Arc-hyperbolic sine function. | — |
| cos | — | ( x ) | Cosine function. | — |
| acos | arccos | ( x ) | Arc-cosine function. | — |
| cosh | — | ( x ) | Hyperbolic cosine function. | — |
| acosh | arccosh | ( x ) | Arc-hyperbolic cosine function. | — |
| tan | — | ( x ) | Tangent function. | — |
| tanh | — | ( x ) | Hyperbolic tangent function. | — |
| atan | arctan | ( x ) | Arc-tangent function. | — |
| atanh | arctanh | ( x ) | Arc-hyperbolic tangent function. | — |
| atan2 | — | ( x, y ) | Atan 2 function. | Same as: atan (x/y) |
| exp | — | ( x ) | Calculates the exponential ex. | — |
| expl | — | ( x, y ) | Calculates the exponential with a maximum value. | Same as: min (exp (x), y) |
| ln | — | ( x ) | The natural logarithm function. | — |
| log10 |  | ( x ) | The base-10 logarithm function. |  |
| log |  | ( x ) | The generic logarithm function. This function is included for legacy compatibility and its use is not recommended. | Normally this is the same as ln(x) except in 'B' arbitrary sources where it is log10(x). This behavior is also changed by the .SYNTAX statements. |
| sqrt | — | ( x ) | Square root function. | — |
| abs | — | ( x ) | Absolute value function. | — |
| sgn | sign | ( x ) | Sign or signum function. | if (x < 0) sgn(x) == -1 if (x > 0) sgn(x) == 1 if (x == 0) sgn(x) == 0 |
| max | — | ( x, y ) | Returns the maximum of x and y. | — |
| min | — | ( x, y ) | Returns the minimum of x and y. | — |
| uramp | — | ( x ) | Ramp function, clips the value against a minimum of 0. | if (x < 0) uramp(x) == 0 if (x >= 0) uramp = x |
| u | stp, step | ( x ) | Step function. | if (x < 0) u(x) == 0 if (x > 0) u(x) == 1 if (x == 0) u(x) == 0.5 |
| table | — | (expr, x1,y1, <x2,y2 <…>>) | Piecewise linear function. Specified x-values must be increasing in value from left to right. Inputs below x1 result in an output equal to y1. Inputs above xn (the largest specified x-value), result in an output equal to yn. In other words, table function acts as a limiter in those regions. Using this function in a Value-type Arbitrary source is functionally equivalent to using the Table-type source. | The following line: E1 out 0 value={Table(v(in), -60m,-4,0,0,140m,43.3)} is functionally equivalent to the following line: E1 out 0 TABLE {v(in)} (-60m,-4,0,0,140m,43.3) |
| limit | — | ( x, a, b ) | Clips the input value x to the range (A,B). | — |
| pwr | — | ( x, y ) | The pwr function. | Same as: abs(x)^y |
| pwrs | — | ( x, y ) | The pwrs function. | if (x < 0) pwrs(x) == -(x**y) if (x >= 0) pwrs(x) == (x**y) |
| ddt |  | (x) | Time Derivative | ddt(v(1)*v(CapVoltagenode)) |
| sdt |  | (x) | Time Integral | 1meg*sdt(I(Vsense)+8) |
| V | — | (node) | Voltage of a node. | Can only be used in non-linear controlled source expressions. |
| V | — | (node1, node2) | Voltage difference of two nodes. | Can only be used in non-linear controlled source expressions. Same as: V(node1)-V(node2) Example: E1 out 0 value={V(1,2)*15} |
| I | — | (voltage source) or (inductor) | Current through a voltage source or an inductor. | Can only be used in non-linear controlled source expressions. Example: E1 out 0 value={I(Vsense)**2 + I(E99)} |
| positive | — | ( x ) | Ensure positive function. | if (x < d) positive(x) = d else positive(x) = x where d is 1.0p |
| negative | — | ( x ) | Ensure negative function. | if (x > -d) negative(x) = -d else negative(x) = x where d is 1.0p |
| nonpos | — | ( x ) | Ensure not-positive function. | if (x > 0) nonpos(x) = 0 else nonpos(x) = x |
| nonneg | — | ( x ) | Ensure not-negative function. | if (x < 0) nonneg(x) = 0 else nonneg(x) = x |
| nonzero | — | ( x ) | Ensure non-zero function. | if (x < d) & (x >= 0) nonzero(x) = d if (x > -d) & (x <= 0) nonzero(x) = -d else nonzero(x) = x where d is 1.0p |
| zero | — | ( x ) | Evaluates x but always returns a value of 0.0. | — |
| one | — | ( x ) | Evaluates x but always returns a value of 1.0. | — |
| schedule | — | (x1,y1, <x2,y2 <…>>) | Schedule function. Gives a value of yN for when time between xN and xN+1. | Time is simulation time. |

Mathematical operators:

| Symbol | Alternate Symbol | Description | Usage |
| --- | --- | --- | --- |
| + |  | Addition. | A + B |
| - |  | Subtraction. | A - B |
| / |  | Division. | A / B |
| * |  | Multiplication. | A * B |
| ** | ^ | Exponentiation (power). | A ** B or A ^ B This can be interpreted differently in other simulators. |
| < |  | Less than. | A < B |
| <= |  | Less than or equal to. | A <= B |
| > |  | Greater than. | A > B |
| >= |  | Greater than or equal to. | A >= B |
| == |  | Equal to. | A == B |
| != |  | Not equal to. | A != B |
| & |  | Logical AND. | A & B |
| ¦ |  | Logical OR. | A ¦ B |
| xor |  | Logical XOR. | A XOR B |
| ? : |  | Ternary if. This operator has two symbols and three operands. | A ? B : C This is the same as IF(A,B,C). |

Built-in constants:

| Symbol | Description | Value |
| --- | --- | --- |
| true | Boolean true value. | 1.0 |
| false | Boolean false value. | 0.0 |
| yes | Alternate form of boolean true value. | 1.0 |
| no | Alternate form of boolean false value. | 0.0 |
| pi | The constant pi. | 3.14159265358979323846 |
| e | The constant e. | 2.71828182844590452353 |
| c | Speed of light. | 2.99792458e8 |
| kelvin | Constant to convert between degrees Kelvin and Celsius, and vice versa. | -273.0 |
| echarge | Electron charge. | 1.602176487e-19 |
| boltz | Boltzmann's constant. | 1.3806503e-23 |
| planck | Planck's constant. | 6.62606896e-34 |
| temp | Current temperature of the simulation in degrees Celsius. | The default is 27, but it can be changed from the simulation options. |
| time | Current time of the simulation in seconds. | Current time of the simulation in seconds (it is constant with respect to circuit variables). |

Additional Notes

- IMPORTANT! Unlike most mathematical languages, Multisim considers the unary minus to have higher precedence than exponentiation (power) operators ** and ^. This means that {-5**2} is +25 while {0-5**2} is -25. Although this is unintuitive, it is standard among SPICE simulators. Use brackets to ensure logical, readable expressions in this case.