Setting of Remote Control

Three methods (Method A/B/C) are provided to set this remote control, any one of which can be used in operation.

A.Code Input Method

Manually turn on the machine you want to remotely control such as TV and VCR. Find the brand of the machine out of the code list, and start setting with the first code under the brand. Repeat steps 2-5 until an appropriate code is found for the machine. If no code enables your remote control to work normally, or the brand of your machine is not on the code list, please turn to B/C method.

1. Find the first code of the machine you want to control out of the code list, for example, 0085, if your first TV bears the brand of SVA.

3.After the indicator light goes on, release the two buttons simultaneously.

2. Hold "Р" button, and then press  Type Select button, for example, press P+TV buttons to set the first TV.

4.Input the four-digit codes that you've found in sequence;

5.The indicator light will go out after completion of code inputting.

6.Check whether other buttons work normally. If yes. setting is successful: if no. please repeat steps 2-5

The indicator light goes out

Comments: The indicator light will twinkle after input of each digit.

B.Manuallv Search Code

1. Manually turn on the machine you want to remotely control such as TV and VCR, and aim your remote control at the deceiving window of the machine.

2. Hold "P" button, and then press Type Select button, for example, press P+TV buttons to set the first TV.

4. Press "P" button again and release it, and the indicator light will start twinkling.

3. After the indicator light goes on, release the two buttons simultaneously.

The indicator light goes on

5.Press POWER button repeatedly until you have turned off/on the machine you want to remotely control, and then press Type Select button you have pressed at step 2.

The indicator light goes out                                The indicator light twinkles

6.Turn on the machine again that you have just turned off, and check whether other buttons work normally. If yes, setting is successful: if no, please repeat steps 2-5 until you find the suitable code for your machine.

Стр.2 -3

С. Full automatic search code method

1.	Manually turn on the home appliance device that you will exercise remote control and put the remote controller facing to the receiving window of the device.

2.	Press once the interface of the device you will set up, for instance TV , and the working indicator flashes once.  The indicator flashes once.

3 . First keep pressing “P” key,

4.	Working	indicator	flashes and at then push down POWER	this moment enter the automatic  key and do not release hands    search mode. until the working indicator lights up.

The indicator lights up	The	indicator	flashes

5. When turning off your TV set, press any key on the remote controller to lock this code.

6. Test the keys on the remote  controller for normal working, for example, press “POWER” key if it can turn off the TV set. The set-up is then finished if it works normally and repeat steps 3-6 if it does not work normally

Remote Control Key Copying Function:

Setting Methods:

1.	Press the “P” key and then press the key to the home appliance that you wish to set (e.g. TV and video tape recorder etc.). Release the key when the Indicator Light lights up. This Remote Control would then enter the Set Mode.

Move away the two hands constantly on

Indicator   turns constantly on

2.	Input the special code: 9980. The Indicator Light would flash. This Remote Control would enter into the Remote Control Key Copying Function Mode.

The indicator flashes

3.	Align the infrared transmission window of the remote control that you wish to copy horizontally (this generally means the infrared transmitting device in front of the Remote Control) with the infrared transmission window of this Remote Control (Please keep a distance of 2cm-5cm) :

4. Press any function key on the Remote Control of your original home appliance and release the key when the indicator light lights up. The data of this function would be immediately copied and transferred to this Remote Control.

5. Press the corresponding key (or any key that you need) on the panel of this Remote Control. The Indicator Light would flash again. The data which you have copied and transferred to this Remote Control has been stored in the corresponding key on this Remote Control. Repeat Steps 4-5 with reference to your needs and copy and transfer the data of each key one by one. Press the "P" key when you have completed copying and transferring the data. Exit and stop the Remote Control Key Copying Function Mode.

There is a special storage capacity in this Remote control for saving the copied functions. When the storage capacity is depleted, the Indicator Lamp would flash 5 times to notify you that the Remote Control can no longer perform the copy and transfer function.

Note:

1.	Each key except the “ P” key and each of the Device key ) on this Remote Control can be selected to perform the copy and transfer function.

A total of 114 key functions can be copied and transferred. All copied data shall be stored under the Code of the selected Device which you have chosen (e.g. the device chosen this time is the TV). In future, whenever you use the Code Searching Function or Code Setting Function to match other devices, the matched Codes that have been copied and transferred shall remain unchanged and be stored unaffected in this Remote Control.

2.	Should you wish to revert to the data stored in the prevailing Code to the data prior to the copying and transferring exercise, please key in Code 9981.

3.	For the same Code in the same device, the newly copied and transferred data would replace the previous data on the same key.

Стр.4-5

Setting of favorable channel

Memorize your favorable channels in “Favorable Channel” by use of this function

Set up method

1.Press “TV ” key to select the device to be set up currently;

2.Press “P” key and do not release, then push “FAV” key, release the two keys after the indicator lights up, input the favorable channel number, and for memorizing more favorable channels, press “P” key after input of a channel number, and then input another channel number and repeat the steps till all the favorable channels are input, press “TV” key, the indicator goes out and the setting is finished (when the working indicator has flashed 5 times, it means that it is fully loaded, no more channel number can be input).

For example: to memorize channels [02], [38], [56] in your favorable channels under the interface of TV, press “P” key + “FAV” and the indicator lights up and then press in turn the [0] ► [2] ► [P]► [3] ►[8] ► [P]►[5]►[6] ► [TV] the working indicator goes out and the setting is finished.

3.In normal use condition, just press “FAV” key toward the TV set and you will call out in turn the set favorable channels, and each time you press “FAV” key you can call out a channel and this can be done repeatedly.

Clear the favorable channels

Operation mode :

- In process of “FAV” setting, you can press “FAV” key for clearing if you make a wrong input or require resetting. Press “FAV” key once and you will clear one command (i.e one key-set code);

- Fully clearing of the favorable channels: First press “P” key and do not release, then press FAV key and release after the indicator is on constantly. Press “FAV” key one by one till the indicator fast flashes three times and it means that the set content is fully cleared and then press any device key to exit.

Note: After exiting from favorable channel setting, remote controller will return to the device state before favorable channel setting and has nothing to do with the device pressed.

Multifunction key setting

This product has two multifunction keys: M1 and М2 . Each multifunction has at most a storage of 20 keys. By using this function, you can combine numbers of succession or regular key control actions into use on one key. After setting, if you press the multifunction key you previously set, the remote controller will send out key control code in the order you previously set, which can simplify the operation.

For example, turn on TV set power -->switch to TV/ VCR - ->turn on VCR power - -> start play ( PLAY)

<1> TV data adding

1.	Press TV key to select the device to be set up currently?

2.	Push down "P" key and do not release, then press the multifunction key "M1" key that you will set and release after the indicator is constantly on;

3.	Press once "POWER" key , which means that the power data code of TV 1has been stored into Ml. Then press “TV/AV” to add a group code (the indicator flashes once when pressing a key).

4.	Press “TV” key, the indicator goes out to exit setting.

<2> VCR data adding

1.	Press “VCR” key to select the device to be set up currently;

2.	Push down “P ” key and do not release, then press the multifunction key " M1 " key that you will set and release after the indicator is constantly on;

3.	Press "POWER" key , which means that VCR power data code has been stored into M1, then press “PLAY” key.

4.	Press any key and the remote controller will exit from the multifunction settings state, the setting is then finished.

Note: After exit from multifunction setting, remote controller will return to the device before multifunction setting and has nothing to do with the device pressed.

Now just put the remote controller toward TV set and press “M1” key (under any device), it will in turn send out data code :

“TV.POWER" + "TV/AV” + "VCR. POWER ” + "PLAY" . and realize: turn on TV set power —>switch to TV/VCR —>turn on VCR power —>start play (PLAY) function

Multifunction key clearing

Operation mode :

1.	In the state of multifunction setting, pressing the corresponding M1 /М2 once will clear one order key;

2.	Fully clear the multifunction key: First press “P” key and do not release, then press the multifunction key "M1/М2 " you will clear and release after the indicator is constantly on; press one by one the multifunction key

"M1 /М2 " till the indicator fast flashes three times, which means it is fully cleared. Press any device key to exit.

Code Lock and Code Unlock Functions

□ The dedicated function for the Swift Code would be defunct should the Code Lock function be set.

Code Lock

Press the “P” key and then the "Device" key (e.g. Select TV) . Input Code 9911 when the Indicator Light lights up. The Code would be locked immediately. No data operation can override this Code. You could not input new Codes to search and change the inputted Codes.

Code Unlock

Press the "P" key and then the "Device" key (e.g. Select TV) . Input Code 9912 when the Indicator Light lights up. The code would be unlocked immediately. You can input data to operate the Remote Control again.

Note:

After locking the Code, you would not be able to switch the home appliances in use. You are unable to input the Codes for the Remote Control until the Codes for the home appliances are unlocked.

Volume Control Function Setting

After setting this Function, you are able to use the volume control function to control the TV device even when the present control mode is not set at TV.

Setting Methods:

1.Press the "P" key and then the "Device" key. Input Code 9901 when the Indicator Light lights up to set the Volume Function;

2.Press the "P" key and then the "Device" key. Input Code 9902 when the Indicator Light lights up to cancel the Volume Function.

Code inquiring mode

After making manual automatic search of the code, perform the following steps

and you will get the code that controls your home appliance device:

- First press "device type selection" key of the home appliance device you search for (such as TV, VCR etc.,) and the indicator will flash once in the meantime .

2.Push down “P ”key and do not release, then press number key “4”on the remote controller and pay attention to the times the indicator flashes. The flashing times of the indicator stands for the number at the units digit of a 4 digit code.

3.	Push down “P ”key and do not release, then press number key “3”on the remote controller and pay attention to the times the indicator flashes. The flashing times of the indicator stands for the number at the tens digit of a 4 digit code.

4. Push down “P ”key and do not release, then press number key “2”on the remote controller and pay attention to the times the indicator flashes. The flashing times of the indicator stands for the number at the hundreds digit of a 4 digit code.

5.Push down “P ’’key and do not release, then press number key “1”on the remote controller and pay attention to the times the indicator flashes. The flashing times of the indicator stands for the number at the thousands digit of a 4 digit code.

Note: In inquiry of a code, no flashing of the indicator means zero.

Стр. 7

Restoring the Factory Settings

Press the “P” key and then the "Device” key. Input Code 9990 when the Indicator Light lights up to restore this Remote Control to the Factory Settings.

Special Note:

1.	Please ensure that the infrared transmission device of this Remote Control is placed horizontally with the transmission device of the remote control of the original home appliance, and that the two remote controls are within working distance.

2.	This Remote Control does not add new function to any home appliances. Should your home appliances not come with the transmission and reception function, this Remote Control cannot be used.

3.	When inserting batteries in this Remote Control, please check and ensure that the batteries are inserted into the compartment in accordance with the polarity displayed.

4.	Should there be improper operation, you may not be able to use and control this Remote Control in the normal manner. You can remove the batteries from the battery compartment, and reinsert the same after 20 minutes for the Remote Control to revert to normal condition.

After Sales Support and Technical Support

Please contact our Company should you encountered any problem while using this Remote Control or should you be unable to operate this Remote Control in the normal manner. Our Company strives to provide you with quality technical support on services and products.

Product Repairs and Maintenance

Our company provides a one year repairs and maintenance warranty to damages not caused by human acts on this Remote Control. Do not open, alter or modify any part of this Remote Control without authority. Our company would not provide any repairs and maintenance services to Remote Controls found to be opened, altered or modified without authority. Our company reserves all right.

Product Specifications

Remote Control Working Distance: Approximately 8 metres Battery Size: Two AAA batteries (DC 3 V)

Weight: Approximately 80 grammes (excluding the batteries)

Our company shall retain the right to the final interpretation to this Users' Manual. Modifications to the design and the specifications to this Remote Control are subject to change without prior notice.

Стр. 8