## Operational Amplifier

The circuit schematic of the typical 741 op-amp is shown below:

A component-level diagram of the common 741 op-amp. Dotted lines outline:

- current mirrors (red)

- differential amplifier (blue)

- class A gain stage (magenta)

- voltage level shifter (green);

- output stage (cyan)

Like all op-amps, the circuit basically consists of three stages:

- Differential amplifier with high input impedance that generates a voltage signal, the amplified voltage difference .

- Voltage amplifier (class A amplification) with a high voltage gain to further amplify the voltage.

- Output amplifier (class AB push-pull emitter follower) with low output impedance and high current driving capability.

The op-amp requires two voltage supplies  of both polarities (typically  V).

Although the Op-amp circuit may look complicated, its operation can be simply modeled by a voltage amplifier with three parameters, as shown below:

- Input resistance , which is huge, typically in the range of , depending on the specific components used (e.g., BJT or FET).

- Output resistance , which is very small, typically a few tens of ohms, e.g., 75 .

- Open-circuit gain, based on both the inverting input  and the non-inverting input :

where  is the differential-mode gain and  is the common-mode gain. It is desired that  and , i.e., the output is only proportional to the difference  between the two inputs. The common-mode rejection ratio (CMRR) is defined as the ratio between differential-mode gain and common-mode gain:

As  is large, typically , the output is approximately

Also, as the output  is in the range between  and  and  is large,  is small (in the micro-volt range), i.e., . If, as in some Op-Amp circuits,  is grounded, then  is very close to zero, i.e., it is almost the same as ground, or virtual ground. The analysis of various op-amp circuits can be much simplified by this virtual ground assumption.

The output of an op-amp is . As  is large,  is usually saturated, equal to either  or , depending on whether or not  is greater than . For  to be meaningful, some kind of feedback is introduced. In the following, we consider the following typical Op-Amp circuits to show how to carry out circuit analysis.

- Voltage follower: The input is connected to the positive input  while the output is directly connected to the negative input  (100% negative feedback), as shown on the left of the figure below. Based on the model of the op-amp shown in the figure above, the follower circuit can be represented as the circuit shown in the middle diagram of the figure below. Our goal here is to build a model for the follower circuit, as shown on the right of the figure, in terms of the input resistance , the output resistance  as well as the voltage gain .

  - Open-circuit voltage gain : Assume an ideal source voltage  () is applied to the input of the circuit and the output port is open circuit . Then applying KVL to the loop, we get

Note that the internal voltage source is . The output voltage is:

and the open-circuit voltage gain is:

Since ,  is approximately unity.

  - Input resistance : We now connect a load  to the output port, while still keeping  (as it is irrelevant to ). Applying KVL to the two loops we get:

Solving these two equations for the loop currents  and  we get

The input resistance can be found as the ratio of the input voltage and current:

Note that  is affected by the load . As usually  is very small in comparison with all other resistances in the expression, it can be dropped and the above becomes approximately

  - Output resistance : This is the ratio  between the open-circuit voltage  and the short-circuit current . We first apply KVL to the loop to find open-circuit voltage  (with  and ):

The voltage across the output port is

We next find short-circuit current  () by applying KVL to the two loops:

Solving these two equation for the two loop currents we get:

Now the output resistance can be found:

Note that  is affected by the internal resistance  of the source. As  and , we have

In summary, we see that the voltage follower has a unit voltage gain, but much increased input resistance  (e.g., ) and much reduced output resistance  (e.g., ). In practice we could simply assume  and .

Example:

The figure on the left shows a circuit represented by an ideal voltage source  in series with an internal resistance  (Thevenin's theorem), with a load . The voltage delivered to the load by this non-ideal source is

The output voltage across the load is only a fraction of the voltage due to the voltage drop across the internal resistance . If it is desired for the output voltage to be as close to the source as possible, the internal resistance  has to be small while the load resistance  has to be large (lighter load). However, given  and , it is still possible for the output voltage to be very close to the source if a voltage follower is used as a buffer between the source and the load, as shown in the figure on the right. The voltage follower is modeled by its input and output resistances  and , as well as its voltage gain , and the output voltage can be obtained after two levels of voltage dividers:

As  is huge, , also, as  is very small, , and , therefore , i.e., one hundred percent of the source voltage is delivered to the load.

- Inverting Amplifier

As the analysis of the circuit using full model of the op-amp is very involved, certain approximation is made the simplify the analysis.

  - Open-circuit voltage gain: We assume . We assume an ideal voltage source  () applied to node  (), and find the input current to be:

where . Solving the equation above for , we get:

The output voltage can be found to be:

i.e.,

The approximation is due to the fact that  is very small and  is very large. The same result can also be obtained under the virtual ground assumption , we can easily find  by applying KCL at the node of :

we get the same .

  - Input resistance: We assume an ideal voltage source  () applied to the circuit, and find the input resistance  as the ratio of  and the input current . We first apply KCL to the node of  to get

Solving for  to get

The input current is

Therefore

As  is much smaller than all other resistances in the equation, it can be dropped:

Moreover, as , we have

  - Output resistance: Here we assume  to simplify the analysis. We first find short-circuit output current by applying KCL to the output node to get:

but as , we have

Next we find the open-circuit output voltage. Applying KCL to the node of  we get

which can be solved for

The open-circuit output voltage can be found to be (voltage dividor)

Now we get

The approximation is due to the assumption that . In particular, if  and , we have

- Non-Inverting Amplifier (Homework)

Find the three parameters of this non-inverting amplifier:

  - input resistance ,

  - output resistance ,

  - open-circuit voltage gain .

Assume  in all three cases. Moreover, assume  for  and , and  for . Note that when , this non-inverting amplifier will become a voltage follower, in terms of all three parameters. Verify your results by checking if this is the case.

Answer

## Op-Amp Circuits

To simplify the analysis of the Op-Amp circuits, we further make the following assumptions:

- The huge input resistance  can be treated as infinity .

- The input current drawn by an op-amp is samll ( ), and could be approximated to be zero .

- The small output impedance  can be treated as zero , i.e., the output  is not affected by the load  (so long as it is much greater than ).

- Based on the fact that , we could assume , i.e., the virtual ground assumption.

- The bandwidth is large ().

Based on these approximations, an Op-Amp can be further simplified as the modeled shown on the right of the figure below, based on which the analysis of op-amp circuits can be much simplified, as shown in the following examples.

- Voltage follower (buffer)

As the output  is the same as the input, why can't we replace this op-amp circuit by a piece of wire?

- Inverter

Current into the op-amp is negligible, and . Applying KCL to the node of , we have

In general,  and  in the inverter can be replaced by two networks (with impedances  and  respectively) containing resistors and capacitors and the analysis of the circuit can be carried out easily in frequency domain:

This is a convenient way to design filters of various frequency characteristics.

- Non-Inverting Amplifier

- Summer-inverter

Apply KCL to :

- Differential amplifier

Define , we get:

But as

therefore

Consider some special cases:

  - If  and , we get

  - If  (open circuit, and  can be any value), then  and we get

This is a combination of inverter and a non-inverter amplifiers.

  - If , then , this is the follower.

  - If  (), then we get the inverter

  - If  () and , we get the non-inverter:

Note 1: It is likely that both inputs are subjected to some common noise  (such as interference of 60Hz power supply):

In this case the output is

not affected by the common noise at all, i.e., the differential amplifier can suppress common-mode signal (such as the noise signal ) while amplify the differential-mode signal (such as  and ).

Note 2: If one of the two inputs, e.g.,  is connected to a constant voltage treated as a reference , then the differential amplifier can also be used as a level shifter. As

we get

But

we have

where

In other words, the output is  times the input , shifted by a constant value . This level-shifter circuit can be used to change the DC level of the signal (e.g., removal of DC component) as well as amplifying it.

- Instrumentation Amplifier

One drawback of the differential amplifier is that its input impedance () may not be high enough if the output impedance of the previous stage is not low enough. To overcome this problem, two non-inverters with high input resistance can be used each for one of the two inputs to the differential amplifier. The resulting circuit is shown below:

The analysis of this circuit is very simple. As the output impedance of the non-inverter is low, the three op-amp circuit can be considered as three independent circuits. The outputs of the two non-inverters are:

The output voltage of the differential amplifier is:

Of course the two resistors  can be combined to become , i.e., , then the output can be written as:

Alternatively, we consider the current going from  to :

From the equation of the first two terms we get:

From the equation of the second two terms we get:

Using the equation of the differential amplifier above, we get the same result as above:

- Algebraic summer (inputs of different signs)

Define . Apply KCL to  and  we get:

Solving the 2nd equation for  we get:

and substitute it into the first equation to get

- A/D converter

Without feedback, the output of an op-amp is . As  is large,  is saturated, equal to either the positive or the negative voltage supply, depending on whether or not  is greater than . These two possible outputs, positive and negative, can be treated as ``1'' and ``0'' of the binary system. The figure shows an A/D converter built by three op-amps to measure voltage  from 0 to 3 volts with resolution 1 V.

Due to the voltage divider, the input voltages to the three op-amps are, respectively, 2.5V, 1.5V and 0.5V. The output of these op-amps are listed below for each of the input voltage levels. A digital logic circuit is then needed to convert the 3-bit output of the op-amps to the two-bit binary representation.

| Voltage (volts) | 0 | 1 | 2 | 3 |
| --- | --- | --- | --- | --- |
| Op-amps Outputs | 000 | 001 | 011 | 111 |
| Binary Representation | 00 | 01 | 10 | 11 |

- First order system -- integrator and differentiator

Integrator

In time domain, as  and , we have (KCL)

where . In frequency domain, we have:

Differentiator

If we swap the resistor and the capacitor, we get in time domain:

In frequency domain, we have:

- First order systems - low-pass and high-pass filters

Low-pass filter:

where , . Intuitively, when frequency is high,  is small and the effect of negative feedback is strong, therefore the output is low.

For example, when , , the Bode plots are shown below:

High-pass filter:

where , . Intuitively, when frequency is low  is large and the signal is difficult to pass, therefore the output is low.

For example, when , , the Bode plots are shown below:

Band-pass filter:

where , , .

For example, when , , , the Bode plots are shown below:

- Higher order systems

Higher than first order systems can be built with multiple integrators, as shown here for a third order system:

From the diagram, we can get

But we also have

i.e.,

we get the transfer function

- Second order system by 2 integrators

From the diagram, we can get

substituting the first two equations into the last one, we get

from which we obtain the transfer function as

which is a second order system. In particular, if , we have

Comparing this with the canonical 2nd order system transfer function

we see that we can let  and . Moreover, , i.e., the feedback from the output should be negative.  is a constant scalar which can take any value.

- Sallen-Key Topology

The Sallen-Key topology is an electronic filter topology used to implement second-order active filters that is particularly valued for its simplicity.

We represent the input and output in s-domain as  and , respectively, and the voltage at node a as , and apply KCL to nodes a and b to get:

Solving the second equation for  we get

Substituting this into the first equation we get

Example 1 , , , , then we get a second order low-pass filter:

where

Example 2 , , , , then we get a second order high-pass filter:

where